## Slide 1: SESSION InITIATION PROTOCOL (sıp)
HISTORY INFO
Erdinç DAĞLI

## Slide 2: SIP is found in the application layer, such as HTTPS. SIP starts, edits, and ends a session. It also manages conference calls. There are also specific tasks, such as adding or removing attendees to an existing session. A dialog is just a series of transactions between two SIP peers. The purpose of a dialog is to setup, possibly modify, and then teardown a session. Hence the name Session Initiation Protocol. A transaction consists of a Request, any non-final (1xx) Responses received, and a final Response (2xx, 3xx, 4xx, 5xx, or 6xx), as well as the acknowledgements of the Responses (ACK or PRACK), except for ACKs to 2xx Responses.
SESSION INITIATION PROTOCOL (SIP)
Notes: SIP defination should be enhanced. Also, please explain DIALOG and TRANSSACTION and difference between them.
Okey.I added new defination for SIP in my words.and also explained DIALOG and TRNSACTION .

## Slide 3: User agent (UA):That ıs general represantatıon of Clıent and server as noted below; User agent clıent (UAC):UAC sends a request and receıves a response user agent server (uas):UAS receıves a request and sends a response Proxy server Stateless Proxy server:It only receives and Forwards the message. Stateful Proxy Server: It keeps track of every request and response received and can use it in future if required.
SESSION INITIATION PROTOCOL (SIP)
  Network Elements

## Slide 4: INVITE : INVITE is used to initiate a session with a user agent. BYE : BYE is the method used to terminate an established session. cancel : CANCEL is used to terminate a session which is not established. ack : ACK is used to acknowledge the final responses to an INVITE method. optıons : OPTIONS method is used to query a user agent or a proxy server about its capabilities and discover its current availability. ınfo : INFO is used by a user agent to send call signalling information to another user agent with which it has established a media session. UPDATE : Modifies the state of a session. refer : Asks the recipient to issue call transfer. subscrıbe : Subscribes for Notification from the notifier. Nofıty : Notifies the subscriber of a new event.
SESSION INITIATION PROTOCOL (SIP)
Request Messages
Notes: Should add UPDATE,REFER,SUBSCRIBE,and NOTIFY SIP requests.
I updated your advices.You may check?

## Slide 5: 1xx:provısıonal /ınformatıonal response: 100 Tryıng 180 rıngıng 181 call ıs beıng forwarded 183 SessIon PRogress 2xx:success response: 200 ok 202 accepted 3xx:Redırectıon response: 300 multıple choıces 301 moved permanently 302 moved temporarıly
SESSION INITIATION PROTOCOL (SIP)
Response Messages

## Slide 6: 4xx:clıent faılure response: 400 bad request 403 forbıdden 404 not found 5xx:server faılure response: 500 server ınternal error 502 bad gateway 6xx:global faılure response: 600 Busy everywhere 603 declıne
SESSION INITIATION PROTOCOL (SIP)
Response Messages

## Slide 7: The fundamental functionality provided by the request history information is the ability to inform proxies and UAs involved in processing a request about the history or progress of that request (rfc 4244) The History-Info header is optional in that neither UAs nor Proxies are required to support it.(rfc 4244) Without the SIP History-Info Header the redirecting/orıgınal called number information would be lost.
SESSION INITIATION PROTOCOL (SIP)
History Info

## Slide 8: The SIP History-Info header is generated by a User Agent or proxy and is passed from one entity to another through requests and responses. The SIP History-Info Header displays the following: -The URI or address that indicates the redirecting number -The reason for the Request-URI or address modification -Chronological ordering of the Request History information
SESSION INITIATION PROTOCOL (SIP)
History Info
Notes: You think ? Is this part okey ? If you want to remove this one.i can remove.because i putted information previos part for SIP History Info. Is it enough ? Or not ?

## Slide 9: For f10 ınvıte, request urı : The Request URI is the contact information of the next hop in the call Route. VIA : The Via header field indicates the path taken by the request so far and helps in routing the responses back along the same path. From : The From header field indicates contact information of the initiator of the SIP INVITE request. To : The To header field contains the information about the called party or the recipient of the request call – ıd : The Call-ID header field is a unique ID identifying the SIP call. Hıstory-ınfo : The header that chronologically (rfc 4244) lists the INVITE and RESPONSEs made by SIP.
SESSION INITIATION PROTOCOL (SIP)
History Info
Notes: Also i added this part.i thought i can show to expalin History Info and Sdp outputs’s shortcuts on the same part. For intelligibility.

## Slide 10: The first part is a SIP output that sends a confirmation response in code 200. The next section gives us more information about the connection with SDP Headers. v=protocol versıon number o=username,ıd,network address.. S =Sessıon name C=connectıon ınformantıon t =tıme the sessıon ıs actıve m=medıa name and transport address (rfc 6157) a=zero or more sessıon attrıbute lınes
SESSION DESCRIPTION PROTOCOL (SDP)
Notes: Replace 4244 with original reference of SDP. RFC-3264 is real reference for SDP but that has been obsoleted with a new one. Please find latest reference for SDP.
I replaced RFC 4244.I founded RFC 6157 but I’m not sure .May you check for me ?

## Slide 11: Alice calls Bob. Bob's proxy determines that Bob is busy, and the proxy forwards the call to Bob's voicemail. (rfc 4458)
SESSION INITIATION PROTOCOL (SIP)
History Info

## Slide 12: Sıp Detaıls and sdp detaıls for f2 Invıte (rfc 4244)
SESSION INITIATION PROTOCOL (SIP)
History Info

## Slide 13: Sıp Detaıls and sdp detaıls for f3 Tryıng (rfc 4244)
SESSION INITIATION PROTOCOL (SIP)
History Info

## Slide 14: Sıp Detaıls and sdp detaıls for f4 moved temporarıly (rfc 4244)
SESSION INITIATION PROTOCOL (SIP)
History Info

## Slide 15: Sıp Detaıls and sdp detaıls for f5 ınvıte (rfc 4244)
SESSION INITIATION PROTOCOL (SIP)
History Info
Notes: Should i replace RFC-4244? Because You said this example is wrong.
What shall i do right now ?

## Slide 16: In this section we can see the spelling difference between RFC-4244 and RFC-4458. rfc -4244 rfc - 4458
SESSION INITIATION PROTOCOL (SIP)
History Info
Notes: I’m not sure about these issues.I went from RFC-4244 to RFC-7044.They were different.I think in RFC-7044 information right.
For RFC-4458 I went from RFC-4458 to RFC-8119.but i didnt found anything for diffrence about syntax in RFC-8119
I putted screenshots on this part but we should to check again with together.

## Slide 17: 1.https://www.wikizeroo.org/index.php?q=aHR0cHM6Ly90ci53aWtpcGVkaWEub3JnL3dpa2kvU0lQ 2. https://www.3cx.com/pbx/sdp/ 3. https://www.tutorialspoint.com/session_initiation_protocol/ 4.https://www.dialogic.com/webhelp/IMG1010/10.5.3/WebHelp/sip_history_info_head.htm 5. https://andrewjprokop.wordpress.com/2014/12/29/a-look-at-how-avaya-aura-supports-sip-based-voice-mail/ 6. https://www.hjp.at/doc/rfc/ 7. https://tools.ietf.org/html/rfc4244#section-4.3.3.2 8. https://tools.ietf.org/html/rfc4458 9. https://tools.ietf.org/html/rfc3261#page-9 10. https://transnexus.com/whitepapers/sip-invite-header-fields/
SESSION INITIATION PROTOCOL (SIP)
Resources
Notes: And last part for my questions.
May this part is stay?
Or may i remove on the there ?
i couldn't sure about that.
Is it necessary for last part?